## Slide 1: Wind-Aware Trajectory Planning for Fixed-Wing Aircraft in Loss of Thrust Emergencies
SASWATA PAUL
FREDERICK HOLE
ALEXANDRA ZYTEK
CARLOS A. VARELA
WORLDWIDE Computing Laboratory
DEPARTMENT OF COMPUTER SCIENCE
Rensselaer Polytechnic Institute
The 37th DASC, London – September, 2018

## Slide 2: Background-Dynamic Data-Driven Avionics Systems
To facilitate development of smarter (flight) data streaming systems, we investigate:
  Programming technology to facilitate modeling spatio-temporal data streaming applications
    PILOTS (ProgrammIng Language for spatiO-Temporal data Streaming applications)
  Error detection using error signatures and error correction based on data redundancy
  Machine learning techniques to infer
  relationships from data
    Offline supervised training
    Online prediction and learning

## Slide 3: US Airways Flight 1549
Need for real-time decision support: US Airways flight 1549
  Caused by birds strike damaging both engines
  The pilots successfully ditched in the Hudson river
Image courtesy: cnn.com
Image courtesy: wikipedia.com

## Slide 4: Dynamic Data Driven Avionics
Our Goal: To create a dynamic data driven trajectory generation system to assist pilots in such situations by taking into consideration dynamic aspects such as partial power, wind, etc.
Our model uses geometric criteria for generating trajectories using different bank angles and corresponding radii of turn and glide ratios for different drag configurations.
Our aircraft model is parameterized on a Baseline Glide Ratio for clean aircraft configuration assuming best gliding airspeed in straight flight.
We dynamically infer the baseline glide ratio to update our model in order to accurately reflect the current performance of the aircraft.

## Slide 5: Dynamic Data Driven Model
Fig: Dynamic Data Driven Flight Trajectory
Generation
Fig: Damaged Aircraft Model

## Slide 6: Low-altitude trajectories
For a given runway and a given bank angle, we have two scenarios:
  Low Altitude scenario:
  In this case, the trajectory consists of a simple Dubins Airplane Path that brings the aircraft to the runway.

## Slide 7: High-altitude trajectories
  High Altitude scenario:
  When a simple Dubins Airplane Path brings the aircraft too high above the runway.
  We find an intermediate point to lose excess altitude by extending the final approach along the runway heading.
  In this case, the trajectory consists of:
    A simple Dubins Airplane Path to bring the aircraft over the runway
    An integral [0,1,2….] number of spiral turns to lose excess altitude
    An Extended Runway of length X ∈ [0, 2πR g/g0 ) if integral number of turns cannot bring the aircraft down to the runway at proper altitude.
    A landing configuration glide ratio and airspeed is assumed for the extended runway segment.

## Slide 8: High-altitude trajectories
High Altitude Scenario where number of spirals > 0

## Slide 9: High-altitude trajectories
High Altitude Scenario where number of spirals = 0

## Slide 10: Extended Runway Segment
We use a dirty (landing) configuration glide ratio in the extended runway segment to make sure that the starting point of this segment is at an altitude from which the aircraft can make it safely to the runway.

## Slide 11: Trajectory Safety Metrics
We introduce safety metrics to evaluate trajectories.
Evaluation of trajectories makes it possible for a pilot to make a better informed choice in a shorter time.
The Metrics are:
  Average altitude
  Average distance from runway
  Average bank angle over height
    measures the occurrence of steep turns near the ground
  Total time
  Extended final runway segment distance
  Number of turns

## Slide 12: Trajectory Safety Metrics
Each metric is normalized relative to the minimum or maximum (whichever is desired) and then evaluated in our safety metric equation
We introduce an Utility Function computed by taking a weighted average of all the metrics
This Utility Function is then used to rank the trajectories generated according to their – higher value of utility function implies better trajectory and a better rank
The utility function can be easily modified to account for other factors like Wind

## Slide 13: Effect of Wind on Trajectories
Wind has a profound impact on the shape of flown trajectories with respect to the ground.
Effect of wind on straight flight Effect of wind on turns

## Slide 14: Effect of Wind on Trajectories
In the presence of wind, turns have ground-tracks that are trochoidal rather than circular.
Straight line flights create ground-tracks that are different (have a crab angle).

## Slide 15: Effect of Wind on Trajectories
Therefore, in the presence of wind the ground-tracks may be significantly altered, taking an aircraft away from the intended runway.
Wind also affects ground-speed -- a tail-wind can increase ground-speed while a head-wind can decrease it; thereby affecting the effective gliding range of a gliding aircraft.
A trajectory generated without considering wind may become invalid in the presence of wind
Therefore, wind has to be considered in the generation phase itself

## Slide 16: Effect of Wind on Trajectories
Parts of a typical trajectory
Our typical trajectory has 5 unique segments
Each segment is affected by wind in a different way

## Slide 17: Effect of Wind on Trajectories
Effect of a 40 knot wind from different directions

## Slide 18: Effect of Wind on Trajectories
Effect of a West-wind of different magnitudes

## Slide 19: Generating Wind-Aware Trajectories
We define the following:
An air trajectory is a trajectory flown with respect to the moving airmass
The corresponding ground trajectory is the 3D projection with respect to the ground frame of reference
A no-wind air trajectory is not corrected for wind and might take an aircraft away from the target runway
A wind-aware air trajectory is corrected for wind so that it can lead an aircraft to a runway in the presence of wind

## Slide 20: Generating Wind-Aware Trajectories
A wind-aware trajectory is a trajectory to a virtual runway, the ground trajectory of which can bring an aircraft to the position of the actual target runway, in the 3D space.
The virtual runway is a point lying in the upwind direction from the target runway.

## Slide 21: Generating Wind-Aware Trajectories
In the presence of horizontal wind, the effective baseline glide ratio (ge) with respect to the ground is different from the aerodynamic baseline glide ratio (g0).
However, the rate of descent remains unaffected by horizontal wind as it has no vertical component.

## Slide 22: Generating Wind-Aware Trajectories
Two conditions need to be met by a valid wind-aware trajectory:
The trajectory must be able to bring the aircraft down to the altitude of the runway.
The end of the trajectory must meet the coordinates of the runway in the two-dimensional space.

## Slide 23: Generating Wind-Aware Trajectories
Therefore, in order to compute valid trajectories, we make the following assumptions:
The aircraft always flies with the best gliding airspeed v.
For each segment in an air trajectory, time t is required to fly that segment with respect to the airmass.
The aircraft follows each segment of the air trajectory for time t.

## Slide 24: Generating Wind-Aware Trajectories
Assumptions 1, 2 and 3 imply that a ground trajectory will lose exactly the same amount of altitude as the corresponding air trajectory since time in air is equal – ensuring Condition I.
The problem is thus reduced to finding a virtual runway such that Condition II holds true.

## Slide 25: Generating Wind-Aware Trajectories
We propose an analytical solution for calculating the virtual runway for trajectories where the Dubins path segment is of the form Right-Straight-Right or Left-Straight-Left.
We also propose a heuristic iterative solution for cases that are not covered by our analytical formula.
We were able to generate wind-aware trajectories in under 50 milliseconds on an Intel Core i7-7500U CPU - 2.70GHz.

## Slide 26: Generating Wind-Aware Trajectories
Heuristic iterative algorithm.

## Slide 27: Generating Wind-Aware Trajectories
Wind-aware trajectory from 5000 feet in 40 knots West-wind
Wind-aware trajectory from 5000 feet in 40 knots West-wind

## Slide 28: Generating Wind-Aware Trajectories
Wind-aware trajectory from 8000 feet in 40 knots West-wind

## Slide 29: Generating Wind-Aware Trajectories
Wind-aware trajectory from 10000 feet in 40 knots West-wind

## Slide 30: Generating Wind-Aware Trajectories
We successfully generated a wind-aware trajectory to LGA31 from an altitude of 3850 feet, assisted by a 30 knots North-wind, even though a no-wind trajectory in the same configuration was not possible.

## Slide 31: Discussion
With a proper wind model, it is possible to design prediction based dynamic data-driven systems that can generate wind-aware 3D trajectories in the event of a loss-of-thrust scenario.
Trajectories generated are of the highest fidelity since they take into consideration the capabilities of the damaged aircraft and the prevailing wind conditions during an actual emergency.
It allows us to compute wind-assisted trajectories when no-wind trajectories are not possible.
Considering wind in the trajectory generation phase itself may present new wind-assisted options or reject options rendered infeasible by wind.

## Slide 32: Questions?
Download open-source PILOTS at:
http://wcl.cs.rpi.edu/pilots
Partial support from:
Air Force Office of Scientific Research
DDDAS Program
Dr. Frederica Darema
(AFOSR Grant No. FA9550-11-1-0332, FA9550-15-1-0214),
National Science Foundation
EAGER/Dynamic Data Program
(NSF Grant No. ECCS 1462342),
MIT Press, June 2013
Consider textbook:

## Slide 33
Extra Slides

## Slide 34: Calculation of Baseline Glide Ratio
Calculation of baseline glide ratio in the MODEL REFINEMENT component:
vt, vt-1, vt-2, vt-3,
Horizontal distance covered in previous 4 seconds
zt, zt-1, zt-2, zt-3,
Altitude loss in previous 4 seconds
Observed Baseline Glide ratio at time instant t
Aircraft sensors

## Slide 35: Calculation of Baseline Glide Ratio
Calculation of baseline glide ratio in the MODEL REFINEMENT component:
ti-1
𝝎
Is standard deviation in 𝝎
< 𝝈T ?
Return baseline glide ratio at time t
To detect window of continuous descent
Taken mean over window 𝝎
To check for stable change in glide ratio in window

## Slide 36: Calculation of Baseline Glide Ratio
With 𝝎=10 and 𝝈T=1: NOT ENOUGH VALUES
US Airways 1549 data

## Slide 37: Calculation of Baseline Glide Ratio
With 𝝎=10 and 𝝈T=20: NOISY
US Airways 1549 data

## Slide 38: Calculation of Baseline Glide Ratio
With 𝝎=2 and 𝝈T=5: NOISY
US Airways 1549 data

## Slide 39: Calculation of Baseline Glide Ratio
With 𝝎=30 and 𝝈T=5: NOT ENOUGH VALUES
US Airways 1549 data

## Slide 40: Calculation of Baseline Glide Ratio
With 𝝎=10 and 𝝈T=5: GOOD
US Airways 1549 data

## Slide 41: Best gliding angle of attack (airspeed)
In order to maximize the gliding distance of the aircraft, the L/D ratio must be maximized by flying at the optimal speed.
Image courtesy: faa.gov

## Slide 42: Effect of bank angle on glide ratio
Fig: Steady-speed engines-out glide ratio vs. airspeed observed in the A320-200
(Avrenli and Dempsey, 2015)

## Slide 43: Loss of thrust aircraft model
Glide ratios and radii of turn for different bank angles for an Airbus A320 at 225 kts
Bank angle has a significant impact on the radius of turn and glide ratio, hence we use different bank angles to generate possible trajectories.

## Slide 44
2D Dubins Path:
  Four options with a straight line segment: LSR, RSR, LSL, RSL
  The shortest one is chosen
RSL
LSL
LSR
RSR
2D Dubins Paths

## Slide 45: Improvements over Existing Work
Fig: (Atkins, 2009) trajectory vs simulator for t+12 sec to LGA 22

## Slide 46: Trajectories with different bank angles
Fig: Effect of bank angle on trajectories.

## Slide 47: Algorithm (Flowchart)

## Slide 48: US Airways 1549
We then ran simulations attempting to recreate the circumstances of the US Airways 1549 incident as closely as possible.
We used bank angles of 20°, 30° and 45°.
The simulations were evaluated using data from the Flight Data Recorder on US Airways 1549
We used a glide ratio of 17.25:1 in a clean configuration during straight flight as predicted by Avrenli et al.
The simulator was used to test the viability and accuracy of the generated trajectories for the US Airways 1549 case.

## Slide 49: US Airways 1549 FDR Data

## Slide 50: Trajectories at t+4
LGA13 LGA22

## Slide 51: Trajectories at t+8
LGA13 LGA22

## Slide 52: Trajectories at t+12
LGA13 LGA22

## Slide 53: Trajectories at t+16
LGA13 LGA22

## Slide 54: Trajectories at t+20
LGA13 LGA22

## Slide 55: Trajectories at t+24
LGA13 LGA22

## Slide 56: Trajectories at t+28
LGA13

## Slide 57: US Airways 1549 Results Summary
Using a glide ratio of 17.25:1, We were able to generate trajectories up to 28 seconds after birds strike, but not for 32 seconds or thereafter.
Runway LGA 13 at La Guardia was reachable for all times up to t+28 seconds.
Runway LGA 22 was reachable for all times up to t+24 seconds.
Runway s LGA31 and LGA 4 were not reachable.

## Slide 58: Trajectory Safety Metrics
We introduce safety metrics to evaluate trajectories.
Evaluation of trajectories makes it possible for a pilot to make a better informed choice in a shorter time.
The Metrics are:
  Average altitude
  Average distance from runway
  Average bank angle over height
    measures the occurrence of steep turns near the ground
  Total time
  Extended final runway segment distance
  Number of turns

## Slide 59: Trajectory Safety Metrics
Each metric is normalized relative to the minimum or maximum (whichever is desired) and then evaluated in our safety metric equation
We introduce an Utility Function computed by taking a weighted average of all the metrics
This Utility Function is then used to rank the trajectories generated according to their – higher value of utility function implies better trajectory and a better rank
The utility function can be easily modified to account for other factors like wind

## Slide 60: Trajectory Ranking Using the Utility Function
Ranking generated trajectories for US Airways 1549 using a glide ratio of 17.25:1

## Slide 61: Further Experimentation and Results
We ran simulations loosely based on the US Airways 1549 incident.
We used bank angles of 20°, 30° and 45°.
The simulations were done for the same initial (latitude, longitude, heading) of the incident, but at different altitudes, for an Airbus A320 with a clean configuration straight flight glide ratio of 19:1 (as shown by the simulator A320 model), under no wind conditions.
We evaluated our generated trajectories on a Precision Flight Controls CAT III Flight Simulator running X-Plane software with an Airbus A320 and no wind conditions.
We evaluated trajectories using our safety metrics.

## Slide 62: Generated vs Sim-Flown LGA 22 (t+8)
Fig: Computed trajectory for LGA 22 (t+8) using a glide ratio 19:1 vs trajectory flown in Flight Simulator.
Notes: Flown with actual wind conditions.

## Slide 63: Low altitude trajectories
Fig: Trajectories to LGA4 from an altitude of 4000 feet
Fig: Trajectories to LGA31 from an altitude of 4000 feet

## Slide 64: High altitude trajectories
Fig: Trajectories to LGA4 from an altitude of 10000 feet
Fig: Trajectories to LGA31 from an altitude of 10000 feet

## Slide 65: Low/high altitude trajectory ranking

## Slide 66: Trajectory Ranking Summary
From 4000ft, LGA 31 at 45 degrees of bank angle is ranked first, due to its extended runway segment, and consistent with avoiding steep bank angles close to the ground.
From 10000ft, lower bank angles are favored with LGA 31 at 20 degrees bank angle being chosen, closely followed by LGA 4 at 20 and 30 degrees of bank angle. This is despite being ranking low on average distance to runway.
The average bank angle / height metric proves really useful in ranking safer trajectories first.

## Slide 67: US Airways 1549 (t+4), g0= 19:1
Fig: Computed trajectory for (t+4) scenario
LGA 22
LGA 13
LGA 31

## Slide 68: US Airways 1549 (t+8) , g0= 19:1
Fig: Computed trajectory for (t+8) scenario
LGA 22
LGA 13
LGA 31

## Slide 69: US Airways 1549 (t+12) , g0= 19:1
Fig: Computed trajectory for (t+12) scenario
LGA 22
LGA 13
LGA 31

## Slide 70: US Airways 1549 (t+16) , g0= 19:1
Fig: Computed trajectory for (t+16) scenario
LGA 22
LGA 13

## Slide 71: US Airways 1549 (t+20) , g0= 19:1
Fig: Computed trajectory for (t+20) scenario
LGA 22
LGA 13

## Slide 72: US Airways 1549 (t+24) , g0= 19:1
Fig: Computed trajectory for (t+24) scenario
LGA 22
LGA 13

## Slide 73: US Airways 1549 (t+28) , g0= 19:1
Fig: Computed trajectory for (t+28) scenario
LGA 22
LGA 13

## Slide 74: US Airways 1549 (t+32) , g0= 19:1
Fig: Computed trajectory for (t+32) scenario
LGA 22
LGA 13

## Slide 75: US Airways 1549 (t+36) , g0= 19:1
Fig: Computed trajectory for (t+36) scenario
LGA 13

## Slide 76: US Airways 1549 Results Summary
Using a glide ratio of 19:1, We were able to generate trajectories up to 36 seconds after birds strike, but not for 40 seconds or thereafter.
Runway LGA 13 at La Guardia was reachable for all times up to t+36 seconds.
Runway LGA 22 was reachable for all times up to t+32 seconds. A left initial turn is recommended at t+28 and t+32.
Runway LGA 31 was reachable up to t+12 seconds.
Runway LGA 4 was not reachable.

## Slide 77: Why DDDAS?
We can distil the aircraft model into purely geometric constraints: Glide Ratios and Radii Of Turn for different bank angles and drag configurations.
We use a Baseline Glide Ratio g0 (the glide ratio for clean configuration with best gliding airspeed in a straight flight) to predict glide ratios for different bank angles and drag configurations.
Allows us to account for dynamic factors such as partial power, wind and effects of surface damage and compute a trajectory corresponding to the current performance capabilities.

## Slide 78: Why DDDAS?
For example, US Airways 1549 data shows some power still available in Engine 1, providing some thrust, resulting in baseline glide ratios of up to 25:1. DDDAS therefore enables more accurate trajectory generation for the emergency at hand.
We could generate valid wind-aware trajectories by using the horizontal wind data in real time.
We could also generate wind-assisted trajectories when trajectories were not possible under no-wind conditions